Firebrick Installation For 82FA

Step 1 RIGHT SIDE- Looking from the front at the unit.

- Stand 6 – 4x9 brick up along the side. The two middle bricks will lay back at a 45 degree angle into the flu cavity. The bricks will lay on an 8x8 piece of steel.

- Place 2 – 4x13 brick horizontal across the top of the 4x9 brick.

- Install largest brick retainer on top of firebrick.

| 4x13 | 4x13 |
| --- | --- |
| 4x9 | 4x9 | 4x9 | 4x9 | 4x9 | 4x9 |

Lay back at 45 degree angle

Step 2 LEFT SIDE

- Place 6 – 4x13 up along the side

- Install the long narrow brick retainer on top of firebrick

| 4x13 | 4x13 | 4x13 | 4x13 | 4x13 | 4x13 |
| --- | --- | --- | --- | --- | --- |

Step 3 REAR OF STOVE

- Place 1 cast iron air vent in left corner.

- Place 2 – 4x9 brick up along the back.

- Place 1 – 4x13 horizontally across the top.

- Install the short piece of angle iron with the extension on top of the firebrick. This should fit snuggly between the 2 side brick retainers.

| 4x13 |
| --- |
| Air Vent | 4x9 | 4x9 |

Step 4 FRONT OF STOVE

- Place cast iron air vent in left corner.

- Place 2 – 4x9 brick up along front wall.

- Install short angle iron on top of bricks. This should fit snuggly between the two side brick retainers.

| Air Vent | 4x9 | 4x9 |
| --- | --- | --- |